## Slide 1
Priyanka Kumari, Veer Bahadur Singh
Optimization and Control of
Gasification Process
Supervised by:
Dr. Rishi Raj

## Slide 2
Background and Motivation
High price of LPG and other fuel
In rural area direct combustion of biomass preferable over LPG
Difficulty in controlling flame of a brick stove.
Blacksmith: directly burning coal.
Highly burning of crops remain/agro-residue in Haryana and Delhi and causes harmful emissions.
Industrial heating
Brick Kilns
Pulp & paper Industries
Small-scale textiles and glass manufacturers
Used by Bhakti Vedanta club for Prasadam cooking.
Source: Internet

## Slide 3
Literature review with summary and research gaps
Gasifier Efficiency (5-10 kW):
Air staging for improved efficiency (Galindo et al., 2014).
Premixing air with producer gas to reduce tar (Jaojaruek et al., 2011).
Need for capacity control and optimization
Stove Comparison:​
Compare fuel usage and indoor air pollution (C. V. Raiyan et al., 1993).​
Burner Fabrication and Optimization:​​
Burners are pivotal components in gasifier systems, ensuring optimal flame quality.​​
Initial design methods (B. Sutar et al., 2016) and specific optimization, particularly in secondary air entrainment, to enhance overall system performance.​​
Quantifying Output and Capacity Control:​​​
Methods include gas analyser, flame analysis, and energy conservation.​​​
Literature favours energy conservation for quantifying gasifier output & capacity control due to cost and equipment availability (Anil K. Rajvanshi et al., FAO 2014).​​​
Control:​​​​
Explore gasification control methods.​​​​
Implement machine learning for real-time monitoring (Elmaz et al., 2020; Mutlu et al., 2018).​​​​

## Slide 4
Gasification: Brief Introduction
Rice Husk
Wood Waste
Rice Straw
Coconut Shell
Bagasse
Source: Kirubakaran et al., Renewable and Sustainable Energy Reviews (2009)
Source: Zanial et al., Biomass and Bioenergy (2002)
Biomass and its Characterization
Producing combustible gas incomplete combustion of biomass​
Based on air supply 3 different types of gasifier are classified​
Updraft, Crossdarft, Downdraft : preferred less tar content
0.38
Air supply

## Slide 5
Problem statements and Solution Approach
Optimize and control of the gasification process.
Experiments on Gasifier and identify operation range (Air)
Producer Gas recirculation in combustion zone
Optimize the amount of producer gas and air for best operation
Check for the suitable control algorithms for such problems
Milestone
Calibration and installation of sensors & actuators.
Design, modification, fabrication and installation of burner.
Design and fabrication and installation of heat exchanger.
Ash Pit
Biomass
Hot Producer Gas
Heat Exchanger with chimney
Hot Air Blower
Producer
Gas
Burner
Proportional valve
Thermocouples
Producer Gas Recirculation
(PGR)
Hot wire anemometer

## Slide 6
Designs and fabrications
Equipment's required
K-type thermocouple => suitable for there temperature range.
Hot wire anemometer => measures the air flow velocity,
Arduino => controls proportional valve,
Proportional valve => controls air flow rate,
Cooling tower => use for the hot water coming out of heat exchanger,
Flow meter => measure water flow rate
½ inch pipe
1½ inch pipe
Source: Sutar et. al., Energy (2016)
Producer Gas Burner
Mass Flow Rate of Flue Gas
Flame Temperature of Flue Gas
Heat Transfer Area required
Sizing of the Heat Exchanger: Red-Bag software
Heat exchanger
Top view
Chimney
Heat exchanger
Source : Anil K. Rajvanshi et al., FAO 2014

## Slide 7
Schematic of Set-up
Physical Set-up
Arduino control system

## Slide 8
Testing of proportional valve with empty gasifier
We are using this to control air flow rate.
Percentage of opening of this valve depends on provided input current.
Air Blower
Proportional Ball Valve
Hot wire Anemometer
Thermocouple
Ball valve
Ash Pit
Proportional Ball Valve
Empty Gasifier
Arduino control system
Vmax 3 m/s
Source: Sensoware

## Slide 9
Preliminarily experiment
Plot of thermocouples
Plot of Tin and Tout of HEx
Observation – No. of holes on the burner top is not enough
Δ T avg 3.6 OC
0.5hr
Amount of pellet used | 5.5 kg | Biomass consumption rate | 2.5 kg/hr
Time of experiment | 2.25 hr | Water flow rate | 10 LPM
AIR

## Slide 10
Calculation for no. of holes
= 2.23kg/h
= ρAV = 0.91 kg/h
/kg biomass 0.41 kg
= 4.6 kg air/kg biomass
Source : Anil K. Rajvanshi et al., FAO 2014
Equivalence ratio() 0.1
From mass balance
=
Gases | Density (kg/m3)
CO | 0.9806
CO2 | 1.5409
H2 | 0.07
N2 | 0.9806
CH4 | 0.5603
O2 | 1.1065
Source – peace software
Assuming
ρ = 0.9886 kg/m3
T avg = = 75 OC = 348K
We are calculating density by weightage average
PG
Air
Gas Mixture
Burner
(120 OC)
(30 OC)
(75 OC)
Ρ = 1.164kg/𝑚^3 | d = 52.48mm | V = 0.1m/s
After air mixing total amount => (1+0.6) 5
Let the total no. of holes = N
Total area A = (N x (πr2)), where D = 2mm
Flow Velocity of each hole V=70 cm/s
= ρAV => N = 640
Heat capacity Q avg = 2.58 kW
(Δ T 3.6OC)
(source: Sutar et. al. Energy (2016))

## Slide 11
Δ T avg 4.5 OC
Δ T avg 5.4 OC
Without PGR
With PGR
Producer gas recirculation(PGR) analysis
1.7hr
0.5hr

## Slide 12
Parametric comparison of the experiments
Parameters | Without PGR | With PGR
Amount of pellet used | 5kg | 5.5kg
Air flow velocity | 0.1 m/s | 0.13m/s
Time of experiment | 2 hr | 3hr
Water flow rate | 10 LPM | 10 LPM
Biomass consumption rate | 2.5 Kg/hr | 1.8 kg/hr
Equivalence ratio () | 0.1 | 0.14
Δ T | 4.5OC | 5.4OC
Q avg | 3.1 kW | 3.7kW
Calorific value of pellets (Source: Kirubakaran et al., Renewable and Sustainable Energy Reviews (2009)) | 18 MJ/kg | 18MJ/kg
Thermal Efficiency of System | 25% | 41%
Parameters | Without PGR | With PGR
Amount of pellet used | 5kg | 5.5kg
Air flow velocity | 0.1 m/s | 0.13m/s
Time of experiment | 2 hr | 3hr
Water flow rate | 10 LPM | 10 LPM
Biomass consumption rate | 2.5 Kg/hr | 1.8 kg/hr
 | 0.1 | 0.14
 | 4.5OC | 5.4OC
Q avg | 3.1 kW | 3.7kW
Calorific value of pellets (Source: Kirubakaran et al., Renewable and Sustainable Energy Reviews (2009)) | 18 MJ/kg | 18MJ/kg
Thermal Efficiency of System | 25% | 41%

## Slide 13
Extended Operation:
  Char incorporation at gasifier bottom.
  Producer gas recirculation in combustion zone.
Temperature Control:
  PGR operation brought early zone temperatures in the range of feasible gasification.
Performance Enhancements (PGR):
  Improved thermal efficiency.
  Heightened flame stability.
Conclusion and Future target
Conclusion
Future target
More experiments with PGR.
Experiments with multi air – staging.
Experiments with different type of biomass.
Fluctuations of anemometer need to be rectify by alternate method.
Optimization and control of system.
Improved Flame Quality:
  Secondary air entrainment in the burner.
  Increased top burner holes.
Old Burner
New Burner

## Slide 14
Time span Activity | 7th Semester |  |  | 2020 |  |  | 8th Semester |  |  | 2022 |  | 
 | Pre mid-sem |  |  | Post mid-sem |  |  | Pre mid-sem |  |  | Post mid-sem |  | 
Literature review |  |  |  |  |  |  |  |  |  |  |  | 
CAD Modeling and Fabrication |  |  |  |  |  |  |  |  |  |  |  | 
Proportional Valve testing and Installation |  |  |  |  |  |  |  |  |  |  |  | 
Completion of Experimental Set-Up |  |  |  |  |  |  |  |  |  |  |  | 
Experiments and parametric analysis |  |  |  |  |  |  |  |  |  |  |  | 
CFD analysis of burner and heat exchanger |  |  |  |  |  |  |  |  |  |  |  | 
Control and optimization via ML |  |  |  |  |  |  |  |  |  |  |  | 
 | Proposed |  |  |  |  |  |  |  |  |  |  | 
 | Completed |  |  |  |  |  |  |  |  |  |  | 
Work Plan

## Slide 15
References
We would like to express our sincere gratitude and appreciation to the following individuals for their invaluable support, guidance, and contributions:
1. Supervisor/Advisor: Dr. Rishi Raj
2. PhD Scholar: Sunil Mehra
3. Resources, infrastructure, and access to research materials: IIT Patna & TFTL
We are truly indebted to each of you for your contributions, encouragement, and belief in the success of this project.
Thank you all.
Acknowledgment
K. Jaojaruek et. al. Bioresource Technology (2011)
Ana L. Galindo, et. al. Biomass and Bioenergy (2014)
Kailasnath B. Sutar et. al. Energy (2016): Burner
Elmaz et. al. Fuel (2020): ML
Mutlu et. al. Enegr (2018): ML
C. V. Raiyan et. al. Atmospheric Environmental (1993): Cooking stove smoke.
V. Kirubakarana et al. Renewable and Sustainable Energy Reviews (2009)
BIOMASS GASIFICATION By Anil K. Rajvanshi
W.1 H2 4U Pty Lt https://h24u.com/types-of-gasifiers/
W.2 Red Bag
www.red-bag.com
W.3 Peace Software https://www.peacesoftware.de/
W.4 Circuital Globe
CircuitalGlobe.com

## Slide 16
Thank you

## Slide 17
Backup slides

## Slide 18
Hot Wire Anemometer works When an electrically heated wire is placed in a flowing gas stream, heat is transferred from the wire to the gas and hence the temperature of the wire reduces, and due to this, the resistance of the wire also changes. This change in resistance of the wire becomes a measure of flow rate.
Thermal (or “hot wire”) anemometers use the principle that the amount of heat removed from a heated temperature sensor by a flowing fluid can be related to that fluid's velocity. These sensors typically use a second, unheated temperature sensor to compensate for variations in the air temperature.
There are two methods of measuring flow rate using a anemometer bridge combination namely:
Constant current method
Constant temperature method
Hot wire anemometer

## Slide 19
Combustion Reaction for Producer gas:
Balancing H :
Balancing C :
Balancing O :
Balancing N :
Air
Hence 1 Kmol of PG needs kmol of air
Producer gas (PG)
Assuming the typical Composition of Producer gas
Raw Producer gas (PG) |  | 
Components | Percentage (vol.%) | Lower Calorific Value
 | 18 | 10
 | 20 | 12
 | 2 | 36
 | 20 | -
 | 40 | -
Raw Producer gas (PG) |  | 
Components | Percentage (vol.%) | 
 | 18 | 
 | 20 | 
 | 2 | 
 | 20 | -
 | 40 | -
As volume fraction for ideal gas can be used as mole fraction

## Slide 20
Design of Shell & Tube Heat Exchanger
Calculation for Mass Flow Rate of Flue Gas
Mass Flow Rate of Flue Gas
PG requires 2.6 Air
Energy Balance In Burner
2. Calculation for Flame Temperature of Flue Gas
3. Heat Duty Range of the Heat Exchanger
Heat Balance In Heat Exchanger
For a gasifier with 1 kg/hr. biomass consumption
For a gasifier with higher capacity for 3 kg/hr. biomass consumption
=>
PG
Air
Flue Gas
Burner
Flue Gas
Water in
Assuming
Assuming
Water out
Source : Anil K. Rajvanshi et al., FAO 2014
=

## Slide 21
4. Sizing of the Heat Exchanger
Tubes of three sizes (½ inch, ¾ inch and 1 inch) are tried and length of heat exchanger is calculated
Shell Diameter is taken as 340 mm (provided the shell must accommodate the burner beneath it)
Tube sheet is designed using online website: www.red-bag.com
1 Inch Schedule 40 Pipe
Number of Tubes (N) = 31
Heat Transfer Area = 0.9
Minimum Length of Heat Exchanger
276 mm
Selected 
Taken length 300mm
Water in
Water Out
300 mm
200 mm
Schedule 40 (14 inch pipe)
Schedule 40 (16 inch pipe)
ID = 358 mm
OD = 379 mm
Cover plate to connect 14 inch and 16 inch pipe

## Slide 22
CAD Model (Full Heat Exchanger with additional Shell)
Exploded View
Burner Area
Baffle
Baffle